## Slide 1
Use cases for ROSA
… Content distribution and CDN interconnect
Paulo Mendes (Airbus), J. Finkhaeuser (Interpeer), Luis Contreras (Telefonica), Dirk Trossen (Huawei)
24.07.2023
IETF117 – ROSA side meeting
https://datatracker.ietf.org/doc/draft-mendes-rtgwg-rosa-use-cases/
https://datatracker.ietf.org/doc/draft-contreras-rtgwg-rosa-gaar/

## Slide 2: Why looking at content distribution
Media content represents the highest portion of traffic on operator’s networks
Media (mostly video) takes the highest share of traffic, being closed to 70%-80% of the traffic on operator’s networks nowadays. This trend will increase with the emergence of new media-based services
Specific overlay platforms, i.e. CDNs, are usually deployed either by operators or over-the-top content providers as a way of optimizing the traffic delivery, in terms of proximity, latency, quality, etc.
Selection of the cache for a specific customer request is based on DNS resolution , with the decisión being taken by the CDN logic currently based on metrics of the proper CDN system (cache status, content availability, hit ratio, etc).
Different ways of improving content distribution based on service-based routing
In a CDN system, the selectable caches can represent different service instances
Two posible ways of improving content distribution
  For live content, improve the overall performance of the service by improving the latency of delivery, providing faster load balance, and simplifying the protection in case of failure
  For VoD content, the storage (i.e., concentration/distribution) and the delivery of those not-so popular but yet demanded (mid-, not short-tail) contents can be more efficiently performed

## Slide 3: Improvement points
Less Time for cache assignment
The time for DNS resolution is removed, thus permitting a faster TTFB and reducing the overall service latency
Better dynamicity on the assignment of caches can take into account routing conditions
Apart from the dynamicity decided by the CDN logic only based on the CDN system status, an additional dimension can be added in a simple manner by incorporating the network status into the service routing decision
Better protection mechanisms for reducing disruption
Protection decision can become simply a (service) routing decision, thus avoiding triggering CDN internal processes for that (protection is on-path)
Extend to distribution of whatever content
From files to any media, i.e., support for any application protocol
Adapt delivery to the nature of the service
CDNs are essentially overlay systems, then overlay-like delivery as the provided by SBR solutions can better fit this kind of systems

## Slide 4: How to make content distribution a SBR-based distribution
Selected contents treated as service routing entries
Not all the contents require SBR treatment
Live contents are limited and temporally available, then becoming a reduced set of SBR entries
Targeted VoD contents to be accessed via SBR would be those not-so popular but yet demanded contents, which gradually can be moved to the popular tier, or to the long-tail tier
  Note that when placing ROSA SAR node into CDN ingress, DNS latencies could be reduced for ALL content types (but only removed for those placed as SBR entries)
Maintain a SBR overlay tailored to the CDN overlay
Contents are dynamically available in different caches, thus the logical overlay for a content is varying on time
SBR can mimic such behavior by adapting the SBR entries as the contents are being made available in distinct caches

## Slide 5
IETF117 – ROSA side meeting
https://datatracker.ietf.org/doc/draft-mendes-rtgwg-rosa-use-cases/
https://datatracker.ietf.org/doc/draft-contreras-rtgwg-rosa-gaar/
THANKS!
24.07.2023
Questions, Opinions, Criticism?